Cloud Chaser
FCC Test Guide
Phillip Sitbon
phillip.sitbon@intel.com

Cloud Chaser is a 900 MHz ISM band radio system using the TI CC1200 radio and CC1190 amplifier with an NXP K66 microcontroller.
The system operates on a fixed set of 25 channels within the 902-928MHz band, hopping on a 40ms interval in a pseudo-random pattern pre-determined by a static address prefix. Every radio network has a single master node which transmits a synchronizing frame every channel cycle. The provided test device is configured as a master by default.
The device’s on-board FCC test command shell provides packet or carrier wave transmission either during normal hopping operation or on selectable channels.
# Console Connection
This device provides a directly accessible command shell via USB CDC-ACM serial connection. To open the command shell, observe the enumerated port name upon device connection (e.g. /dev/ttyACM0 in Linux) and open within a terminal tool such as screen or minicom with a baud rate of 115200. The terminal is simplistic and does not allow escape sequences, arrow keys, backspace or delete. A prompt should appear when pressing enter with an empty command.
# Test Commands
### info [chan]
When called with the chan option, lists all channel numbers and frequencies in hopping order.
Without the chan option, this command shows current device information:
address: <network>.<node>
The network ID defines the pseudo-random hopping pattern. This value is fixed for test devices. The node ID is unique within a given network.
uptime
Indicates how long the device has been operational.
channel
When fixed to an individual channel via test commands, indicates the current channel/frequency. The device will remain on this channel until changed or hopping is enabled.
power
Current power level in percent, not to exceed 27dBm at 100% when high-gain mode (HGM) is enabled.
hgm
Indicates whether the CC1190 high-gain mode (HGM) is enabled.
stats: rx=packets/bytes/errors tx=packets/bytes/errors
Shows raw RF send/receive totals.

### master <enable|disable> [nosync]
Enable or disable master (hopping) mode. With the nosync option, does not send a synchronizing packet every cycle (and non-master nodes will not be able to synchronize or hop as a result).
### chan <0-24>
Manually select a channel. Disables hopping mode.
### send <size:0-115> <count>
Transmit a packet of the selected size, count number of times. The command does not complete until all packets are sent.
### cw <enable|disable>
Enable or disable carrier wave transmission. Can be on while hopping and transmitting packets (including the master sync packet) will temporarily pause CW transmission.
### pwr <0-100>
Set the output gain.
### hgm <enable|disable>
Enable or disable high-gain mode (HGM). This provides gain for both the the TX PA and the RX LNA.
### reboot
Reboot the device.